## Slide 1
Lecturer:
Simon Winberg
Digital Systems
EEE4084F
Lecture 17
RC Architectures Case Studies
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)
Microprocessor-based:
Cell Broadband Engine Architecture
FPGA-based:
PAM, VCC, SPLASH …

## Slide 2: Lecture Overview
Case study of RC computers
  IBM Blade & Cell Processor
  Programmable Active Memories (PAM)
  Virtual Computer Corporation (VCC)
  Super Computer Research Center Splash System
  Small RC Systems

## Slide 3: IBM Blade & The Cell Processor
CASE STUDY:
  Cell (or Meta-) processors
  Changeable in smaller parts – the ‘Strategic Processing Units’ (SPUs) and their interconnects
IBM Blade rack

## Slide 4: The “Cell Processor” : Cell Broadband Engine Architecture Processor
Developed by STI alliance, a collaboration of Sony, Sony Computer Entertainment, Toshiba, and IBM.
Why Cell?
  Actually “Cell” is a shortening for “Cell Broadband Engine Architecture”
  Technically abbreviated as CBEA in full, alternatively “Cell BE”.
The design and first implementation of the Cell:
  Performed at STI Design Center in Austin, Texas
  Carried out over a 4-year period from March 2001
  Budget approx. 400 million USD
Information based mainly on http://en.wikipedia.org/wiki/Cell_(microprocessor)
Image of the Cell processor

## Slide 5: The Cell Processor Milestones
2005 Feb[1,2]
  IBM’s technical disclosures of cell processors quickly led to new platforms & toolsets [2]
Oct 05: Mercury Cell Blade
Nov 05: Open Source SDK & Simulator
Feb 06: IBM Cell Blade
Resources / further reading
  http://www-128.ibm.com/developerworks/power/cell/
  http://www.research.ibm.com/cell/
    (see copy of condensed article: Lect17 - The Cell architecture.pdf)
[2] http://www.scei.co.jp/corporate/release/pdf/051110e.pdf
[1] IBM press release 7-Feb-2005: http://www-03.ibm.com/press/us/en/pressrelease/7502.wss

## Slide 6: Cell Processor Hardware
9 cores
  1 x Power Processor
  8 x Synergistic Processor Element (SPE)
  10 threads (2x PPE threads + 8x SPE threads)
Transistors: 241x106
Size: 235 mm2
Clock: 3.2 GHz
Cell ver. 1: 64-bit arch
Power
Processor
Element
L2 Cache
(512 Kb)
Rambus XRAM ™ Interface
Memory Controller
SPE
IO Controller
Rambus FlexIO™
SPE
SPE
SPE
SPE
SPE
SPE
SPE
Layout of Cell processor adapted from
  http://www.research.ibm.com/cell/
Element interconnect bus
Test&Debug

## Slide 7: Synergistic Processing Element (SPE)
Cells: heterogeneous multi-core system architecture
  Power cell element for control tasks
  Synergistic Processing Elements for data-intensive processing
Each SPE
  Synergistic Processor Unit (SPU)
  Synergistic Memory Flow Control (MFC)
    Data movement and synchronization
    Interface to high-performance Element Interconnect Bus (EIB)

## Slide 8: Cell Broadband Architecture Design
  Synergistic Processor Unit (SPU)
  Synergistic Memory Flow Control (MFC)
EIB
L2 Cache
MIC
MIC
XRAM ™
FLEX™ IO
SPU
MFC
SPE
SPU
MFC
SPE
SPU
MFC
SPE
SPU
MFC
SPE
SPU
MFC
SPE
SPU
MFC
SPE
SPU
MFC
SPE
SPU
MFC
SPE
PPU
PPU

## Slide 9: Programming Extensions
Application Binary Interface (ABI) Specifications
  Defines: data types, register usage, calling conventions, and object formats to ensure compatibility of code generators and portability of code.
Examples
  IBM SPE (Strategic Processor Elements) ABI
  Linux Cell ABI

## Slide 10: IBM SPE for Cell Processors
SPE C/C++ Language Extensions
  Defines: standardized data types, compiler directives, and language extensions used to make use of SIMD capabilities in the core

## Slide 11: Cell Processor Programming Models
Reconfigurable Computing

## Slide 12: Cell Processor Programming Models
Cell Processor change SPEs according to application
Models
  Application-specific accelerators
  Function offloading
  Computation acceleration
  Heterogeneous multi-threading

## Slide 13: Application Specific Accelerators Example
PPE
SPE 1
SPE 2
SPE 3
SPE 4
SPE 5
SPE 6
SPE 7
SPE 8
EIB
Hardware
Software
Software
3D Visualization Application
3D Graphics Acceleration
Texture
mapping
Data
decompression
Data comparison and classification
3D Scene Generation
FLEX™ IO
DATA
Stores

## Slide 14: Function offloading models…
PPE
SPE
SPE
SPE
  Multi-staged pipeline
  Parallel stage of processing
  sequence
PPE
SPE
SPE
SPE
  Remember:
  All the SPEs can access the
  shared memory directly via the
  EIB (element interconnect bus)
  Example:
  LZH_compress(‘data.dat’)
  Example:
  Matrix X,Y
  Y = quicksort(X)
  m = Max(X)
  X = X + 1

## Slide 15: Computation Acceleration
PPE
SPE1
  Similar to model for functional offloading, except each SPE can be busy with other forms of related computation, but tasks not necessarily directly dependent (i.e. the main task isn’t always blocked, waiting for the others to complete)
SPE3
SPE2
Task
#1
Task
#2
Task
#3
  Set of specific computation tasks scheduled optimally, each possibly needing multiple SPEs and PPE resources
SPE4
Processing
resource
usage
SPE1 configured for tasks of type #1
SPE2 configured for tasks of type #2
SPE3 and SPE4 configured for tasks of type #3

## Slide 16: Heterogeneous multi-threading
PPE
SPE1
SPE2
SPE3
SPE4
SPE5
SPE6
SPE7
SPE8
Spawn new threads as needed
Thread
#3
Thread
#3
Thread
#5
All SPEs configured to handle general types of tasks required by the application
Combination of PPE threads and SPE threads
Thread
#1
Thread
#4
Processing resource
usage
disabled processing resources
PPE configured for thread types #1 and #2
SPE1 configured for threads of type #6
SPE2 configured for threads of type #3
SPE3 and SPE4 for threads of type #5
No threads of type #6 currently exist
Certain SPEs configured to speed certain threads, but able to handle other threads also
waiting
(this thread is blocked)

## Slide 17: Designing for performance
Three-step approach for application operation
Step 1 : Staging
  Telling the SPEs what they are to do
  Applying computation parameters
PPE
L2 Cache
Main Memory
SPE
SPE
SPE
SPE
SPE
SPE
SPE
SPE
todo
todo
todo
todo
todo
todo
todo
todo
assigning tasks

## Slide 18: Designing for performance
Step 1 : Staging
  Each SPE can use a different block of memory
Step 2 : Processing
  Each SPE does its assigned task
PPE
L2 Cache
Main Memory
SPE
SPE
SPE
SPE
SPE
SPE
SPE
SPE
1
3
5
7
2
4
6
8
Each SPE uses its allocated
part of memory

## Slide 19: Designing for performance
Step 1 : Staging
Step 2 : Processing
Step 3 : Combination
PPE
L2 Cache
Main Memory
SPE
SPE
SPE
SPE
SPE
SPE
SPE
SPE
1
3
5
7
2
4
6
8
Power PC combines results that
were left by the SPEs in memory,
using its L2 cache to speed it up

## Slide 20: IBM Blade
Each blade contains
  Two cell processors
  IO controller devices
  XDRAM memory
  IBM Blade center interface

## Slide 21: RC Systems
A look at platforms architectures

## Slide 22: Large RC System - PAM
Programmable Active Memories (PAM)
  Produced by Digital Equipment Corp (DEC)
  Used Xilinx XC3000 FPGAs
  Independent banks of fast static RAM
Host
CPU
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
DRAM
Digital Equipment Corp. PAM system (1980s)
Image adapted from Hauck and Dehon (2008) Ch3

## Slide 23: Large RC System - VCC
Virtual Computer Corporation (VCC)
First commercially commercial RC platform*
Checkerboard layout of
  Xilinx XC4010 devices and
  I-Cube programmable interconnection devices
  SRAM modules on the edges
* Hauck and Dehon (2008)
…
…
…
…
…
…
…
…
…
…
…
VCC Virtual Computer
FPGA
SRAM
SRAM
FPGA
FPGA
SRAM
I-Cube
FPGA
FPGA
FPGA
I-Cube
FPGA
I-Cube
I-Cube
FPGA
SRAM
SRAM
FPGA
FPGA
FPGA
I-Cube
I-Cube
FPGA
SRAM

## Slide 24: Large RC System - Splash
Summary of the Splash system
Developed initially to solve the problem of mapping the human genome and other similar problems. Design follows a reconfigurable linear logic array. The SPLASH aimed to give a Sun computer better than supercomputer performance for a certain types of problems. At the time, the performance of SPLASH was shown to outperform a Cray 2 by a factor of 325. FPGAs were used to build SPLASH, a cross between a specialized hardware board but more flexible like a supercomputer. The SPLASH system consists of software and hardware which plugs into two slots of a Sun workstation. **
* Hauck and Dehon (2008)
SRC Splash version 2
Dedicated
controller
…
…
…
…
SRAM
FPGA
FPGA
SRAM
FPGA
SRAM
FPGA
SRAM
FPGA
SRAM
FPGA
SRAM
FPGA
SRAM
Crossbar
Dev. by Super Computer Research (SCR) Center ~1990
Well utilized (compared to previous systems).
Comprised linear array of FPGAs each with own SRAM *
**Adapted from: Waugh, T.C., "Field programmable gate array key to reconfigurable array outperforming supercomputers," Custom Integrated Circuits Conference, 1991., Proceedings of the IEEE 1991 , vol., no., pp.6.6/1,6.6/4, 12-15 May 1991 doi: 10.1109/CICC.1991.164051
Illustration of the
SPLASH design
(adapted from *)

## Slide 25: Small RC Systems
Brown University’s PRISM
  Single FPGA co-processor in each computer in a cluster
  Main CPUs offloading parallelized functions to FPGA
Algotronix
  Configurable Array Logic (CAL) – FPGA featuring very simple logic cells (compared to other FPGAs)
  Later become XC6200 (when CAL bought by Xilinx)
* Hauck and Dehon (2008)

## Slide 26: Reconfigurable Supercomputers
Cray Research
  XD1: 12 processing nodes
  6x ADM Opteron processors
  6x Reconfigurable nodes built from Xilinx Vertex 4
  Each XD1 in own chassis, can connect up to 12 chassis in a cabined (i.e. 144 processing nodes)
SRC
  Traditional processor + reconfig. processing unit
  Based on Xilinx Virtex FPGAs
Silicon Graphics
  RASP (reconfigurable application-specific processor)
  Blade-type approach of smaller boards plugging into larger ones
Ref: Hauck and Dehon Ch3 (2008)

## Slide 27: Additional Reading
Reading
  Reconfigurable Computing: A Survey of Systems and Software (ACM Survey) *
* Compton & Hauck (2002) .“Reconfigurable Computing: A Survey of Systems and Software” In ACM Computing Surveys, Vol. 34, No. 2, June 2002, pp. 171–210.
  (not specifically examined, but can help you develop insights that help you demonstrate a deeper understanding to problems)
-- End of the Cell Processor case study --

## Slide 28: Conclusion & Plans
Reading
  Hauck, Scott (1998). “The Roles of FPGAs in Reprogrammable Systems” In Proceedings of the IEEE. 86(4) pp. 615-639.
Next lecture:
  Amdahl’s Law
  Discussion of YODA phase 1

## Slide 29
Image sources:
IBM Blade rack (slide 3), IBM blade, Checkered flag – Wikipedia open commons
NASCAR image – flickr CC2 share alike
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).